## Slide 1
Introduction to ROS
From zero to a functional communication scheme

## Slide 2: Schedule
Day 1 content
  What is ROS
  How is ROS communication done
  Terminal tools
  Talker and listener
  ROS Launch
Day 2 content
  More advanced ROS concepts
  Activity
  Questions

## Slide 3: ROS basics What is ROS ?
“ROS is an open-source framework that helps researchers and developers build and reuse code between robotics applications”

## Slide 4: ROS basics The conceptual idea behind ROS
University
/ROS
Teacher 1
Student A
Student B
/ROS
/Control
Teacher 2
Student D
Student C
/Control
/Weekend
/Party

## Slide 5: ROS basics What is the information delivered?
Any class has a certain format, which both the teacher and the student know off and is expected to be followed.
Between two friends you are not expecting a power point presentation but some plain text.
Teacher
Students
Presentation and a
practical explanation
Student
Student
Plain text and memes
/ROS
/Weekend
Publishers
Data types
Subscribers

## Slide 6: ROS basics ROS versions and installation
New versions of ROS are released with each Linux distributions, due to compatibility in this course we are going to be working with ROS melodic (released with Ubuntu 18.04).
Currently there’s another version of ROS available for Ubuntu 20.04 and a revision of the ROS structure, known as ROS2, that aims to increase the robustness of the framework for industrial applications and distributed systems. Furthermore, ROS2 allows real time applications.

## Slide 7: ROS Architecture ROS Master
Brain of ROS -> Process manager that enables the communication between different agents in the network.
Allows communication between different computers or robots by means of a Server – Client architecture
ROS Serial
TCP IP Com
ROS Master
User
Node 1
User
Node 2
Robot
Node
Micro.
Node

## Slide 8: ROS Architecture nodes and topics
Piece of software that acts as an element in the network.
It is in charge of executing a part of the code and can be programmed in Cpp, Python or Lisp.
Each topic has a unique msg type.
Node
White line detection
node
Obstacle detection
node
Hardware
Node
Get
data
/Image
Cables
Node

## Slide 9: ROS Architecture messages
  float 32 data
  std_msgs/Header header
  uint32 seq time stamp string frame_id geometry_msgs/Pose pose
  geometry_msgs/Point position
  float64 x float64 y float64 z geometry_msgs/Quaternion orientation
  float64 x float64 y float64 z float64 w
  std_msgs/Header header uint32 height uint32 width string encoding uint8 is_bigendian uint32 step uint8[] data
sensor_msgs/Image
std_msgs/Float32
geometry_msgs/PoseStamped

## Slide 10: ROS Architecture Services and actions
While topics are one way communication, services and actions allow feedback and prevent unnecessary load in the network.
Services follow a question-answer structure, while actions are designed to execute a task and give feedback during the process.
Planning Node
Control Node
Can you send me a path ?
Updated path
Service
Control Node
User Input Node
Move to point A
Success !
Action
Updates:
Current pose

## Slide 11: ROS Architecture Services and actions
int64 a
int64 b
Request
int64 c
Response
int64 a
int64 b
Request
int64 d
Response
int64 c
Feedback
Service
Actions
When defining either an action or a service we need to stablish each member involved in the communication. Usually both are project dependent, so users define their own structures.
-----------------
-----------------
-----------------

## Slide 12: ROS Architecture A practical example
PC

## Slide 13: ROS Architecture Overview
Ros Master
Physical System
ROS Implementation
Control
Node
User
Node
Jetson
Sensors
Node
Actuators
Node
Micro

## Slide 14: ROS Architecture ROS Packages
Ros Packages are a way of organizing codes related between each other.
The same way teachers are gathered within the Engineering school nodes are gathered in ROS packages
Engineering School
ElecEng
MechEng
ChemEng
CompSci
Camera Package
Video
recording
Data acquisition
Video display

## Slide 15: ROS Code Talker and listener framework
Simplest communication scheme.

## Slide 16: ROS Code Talker
#!/usr/bin/env python import rospy from std_msgs.msg import String
if __name__ == '__main__': pub = rospy.Publisher("chatter", String, queue_size=10) rospy.init_node("talker") rate = rospy.Rate(10)
while not rospy.is_shutdown(): hello_str = "hello world %s" % rospy.get_time() pub.publish(hello_str)
rate.sleep()
Terminal Commands
  roscore
  rosrun basic_comms talker.py
  rostopic echo /chatter
Setup environment and import libraries
Create variables and setup node
Publish message
Wait to run again

## Slide 17: ROS Code Listener
#!/usr/bin/env python import rospy from std_msgs.msg import String
def callback(msg): rospy.loginfo("I heard %s", msg.data)
if __name__ == '__main__': rospy.init_node('listener') rospy.Subscriber("chatter", String, callback)
rospy.spin()
Terminal Commands
  roscore
  rosrun basic_comms listener.py
  rostopic pub /chatter <tab complete>
Setup environment and import libraries
Define Callback
Create variables and initialise node
Continuously check for new messages

## Slide 18: ROS Tools ROS Terminal tools
roscore
  Must be executed before working with ros
  Handles the correct functionality of the network
rostopic
  Contains useful tools related with topics
  rostopic echo [topic name]
  rostopic list
  rostopic hz [topic name]
rosrun
  Executes a given node
  rosrun [package] [node name]
rosnode
  Contains useful tools related with nodes
  rosnode list
  rostopic info [node]

## Slide 19: ROS Tools ROS Terminal tools II
roslaunch
  Allows to launch multiple nodes with a single command by calling .launch files
  roslaunch [package] [.launch]
rosbag
  Records the activity of the topics in the network
  rosbag record
  rosbag info [bag file]
  rosbag play [bag file]
config files
  Load parameters into the system that can be accessed by any node
rqt
  ROS visualization tool that provides graphical information of the system status

## Slide 20: Activity Implement a listener-talker
Implement the code in either Python or Cpp.
Use some of the command line tools to verify the correct functioning of the system.

## Slide 21: ROS Tools ROS Parameter Server
ROS allows to load variables into the master which are accessible by all the nodes of the system.
Typically, a .yaml file is loaded into the system through a launch file and configuration parameters are stored there.
They are used them when loading robot models or constants that may vary in different scenarios where the same code is applied.
You will see an example of them in further days of the course
Planning Node
Control Node
roslaunch
Config.yaml
ROS Core
Parameter Server

## Slide 22: ROS Tools ROS Launch
Config files
Master
Node 1
Node 2
ROS Launch

## Slide 23: ROS Tools ROS Launch Syntax
Launch files are sets of commands written in xml that allow executing various scripts at the same time.
The general syntaxis is the following
  <?xml version=“1.0”?>
  <launch>
  [Body of the launchfile]
  </launch>
This syntaxis allows to run any object used within the ROS architecture and has a wide variety of tools that allow to parametrize the launch file so that it can be adapted to the requirements of you project.
An extensive documentation can be found in http://wiki.ros.org/roslaunch

## Slide 24: ROS Tools ROS Launch code tools
Running a node
  <node name=“listener” pkg=“basic_comms” type=“listener.py” output=“screen”/>
Running another file or launch file
  <include file="$(dirname)/other.launch" />
Set parameters
  <param name="publish_frequency" type="double" value="10.0" />
Pass args to the launch file
  <arg name=”camera_id" value=”cam_3" />
Load files into the system
  <rosparam command="load" file="$(find package_name)/config/file_name.yaml" />

## Slide 25: ROS Tools ROS File structure
ROS projects are organized using workspaces, which are a collection of grouped codes called packages.
Instructions for the compiler need to be allocated in .cmake and package files
Package files are exportable between projects
Configuration files used to stablish code dependencies
Code that we will execute
Catkin_make will generate ‘src’ and ‘devel’ for you when compiling the workspace

## Slide 26: ROS Tools ROS Compilation tools
ROS requires to compile each package, generating dependencies related with other packages, external libraries or custom messages, services and actions.
The preferred compilation tool is known as catkin and uses two separated files, package.xml and CMakeLists.txt.
A useful command to create packages is:
  catkin_create_pkg [name] [list of dependencies]
Which generates an empty package and templates of both CMakeLists and package files.
More information about the syntaxis of this files can be found In http://wiki.ros.org/ROS/Tutorials/CreatingPackage
Projects are compiled with the instruction catkin_make and the instruction source [project]/devel/setup.bash needs to be executed to load the changes.

## Slide 27: Example Using custom messages
Create a folder called msg in your workspace.
Make a custom msg definition with a Header and a Float32.
Open both CMakeLists and package.xml and modify them to compile our new msg.
Modify the code of the previous activity using the new msg definition.
  String date String hour
package/time_msg.msg

## Slide 28: Activity Problem architecture
Ros Master
ROS Implementation
Control
Node
User
Node
Simulator
Model
Node
Task

## Slide 29: Activity Teleoperate a PuzzleBot
Teleoperation
Square
Input in the terminal the commands to move the robot
See how the robot traverses accordingly the environment.

## Slide 30: Activity Moving a PuzzleBot
Straight line
Square
Drive the robot in a straight line.
Drive the robot making a square with a side length of 1m.

## Slide 31: Activity How is the robot modelled?
The resultant forward velocity through (the centre of mass) is .
The steering velocity is .

## Slide 32: Activity Some tips and tricks
One publisher cmd_vel
cmd_vel – from geometry_msgs.msg import Twist – 3 linear and 3 angular velocities.
  msg.linear.x, msg.linear.y, msg.linear.z
  msg.angular.x, msg.angular.y, msg.angular.z
Use the equations below to compute the distance moved and the angle turned by the robot
where is the radius of the wheels (=0.05m) and is the distance between the wheels (=0.18m)
Use rospy.get_time() to measure the time between each loop
If the robot is not moving, check your topics with rostopic echo and rostopic pub
Ensure your python file is executable: sudo chmod +x <path_to_file>.py